USB-Fm-Transmitter 0,15 Watt / Radio is a amazing simpel medium. Just some electronic components are enough for transmitting a radioshow. The small USB-FM-Transmitter transforms your computer into a relay station. It can pick up any audio signal from your computer and send it over the UKW-band. (ultrashort wave) / This transmitter is module for a emancipatory society. / How to / Our selfmade circuit board has now holes. All components get soldered on the board. See the example. / Attention: The two transistors and the LEDs have a polarity! Take care how the transistors are placed on the layout. Cut first the +(positiv =A) longer leg of the LED and solder it and then cut the and solder the shorter second leg (- =K) / The stereo NF-connection cable must be transferred into mono cable by bridging the wires. Means you have to hot-wire the red and the white wire by twisting the ends together after you have remove insulation before. / Twist also copper part together. Its the ground part. / After soldering all parts and connecting the board with your computer the red LED should glow. Then you try to find a frequency on your variable capacitor. Don't take a metal part for spinning around. Take something wooden or cardboard. / Parts-List / 1 x 520 Ω (green-brown-brown) / 1 x 100 kΩ (brown-black-yellow) / 2 x 1MΩ (brown-black-green) / 1 x capacitor 0,1µF (0,1) / 1 x capacitor 47 nF (0,047) / 1 x capacitor 4,7pF (479) / 2 x capacitor 22pF (22) / 1 x variable capacitor 1,5 15pF / 2 x transistors BF246 (F246A) / 1 x LED red / 1 x NF-connection (mini-jack) / 1 x USB for power connection

What to bring

Cabel striper
long nose pliers – holding parts
This kind of plier – for cutting and holding parts
Solder Station – please tell us if you need one if you don't have
Solder – will be also there

	Mini-Jack – you can recycle one!
	We just need the USBconnector you can recycle one of this size.
	FM-Radio
Laptop	You can bring as well your own laptop to test.